## Slide 1: ANIRISC-V
By: Anirudh Kashyap, Vishnu Jagan, Ethan John

## Slide 2: Advanced Features
Cache
  L2 Cache
    2 way 16 set L2 cache acts as an intermediate between given cache and memory
  Eviction Write Buffer
    Buffer holds stores dirty evicted lines, allows memory to be read from first
Branch Prediction
  Tournament Branch Predictor
    Chooses between local and global table to decide which one is better using two bit counter
Prefetching
  PC Based Stride Prefetching
    Built into the arbiter, the stride prefetcher remembers distance to previous memory access and prefetches data using that stride
    Falls back on prefetching the next instruction cache line if there is a hit for the given stride forward

## Slide 3: Quantitative Analysis of advanced feature code
Branch predictor above 60% for competition code. 77% on cp3 code.
  To track, used perf counter on testbench by tracking cmp results when branch in ex phase
  5% performance increase compared to static not taken
  Static taken performs better by 2%. Loops with 200 iterations (on test 3 for example) will be taken 99% of the time, so just static taken performs better.
The stride prefetcher with fallback on next instruction prefetching
  This hybrid prefetching scheme got around an average of 10% reduction in runtime across the competition codes
  The prefetcher does best with regular memory accesses in a loop in the case of stride prefetcher and code with no branches for the instruction prefetching
L2 cache was the biggest performance booster. ~60% reduction in execution time
  Parameterized

## Slide 4: Possible Improvements
Biggest: Understanding of what CP3 test code entailed
  Did not realize CP3 test code was much more in depth than CP2 Test Code
    Decent amount of time spent on this, we built a grading harness that printed out register writes, memory loads and stores, and jumps and branches
    We diffed this output with a working mp2 cpu and had another python script that outputted the simulation time of the error on both mp2/mp4
    Knowing the exact time allowed us to easily run and see all signals to compare from mp2/4
    If we had a week to do advanced features, we would look into implementing a trace cache, and potentially a fully associative L2 cache
  Due to a few bugs with our CP3 test code, we had to focus on that more than building extravagant features
CP1 and CP2 {Things we would have changed in CP1 and CP2}
  RVFI MON from beginning, had we figured this out initially, our lives would have been easier as we wouldn’t need to build a grading harness
Design Comp
  Had we a bit more time, we would have made several levels of cache and implemented full associativity as well as a large number of sets, we found this in our L2 cache to have a big decrease in runtime